###### System Data
The system data descriptions provided in this appendix determine the information stored within webMIP for Meter Modules, Housing, Base and pricing elements. These elements will be controlled through the administration functions provided by webMIP.
###### Meter Modules
A meter module is the logical grouping of:
1. a meter to measure the flow of gas to a property;
2. a relief valve to protect the meter;
3. a slamshut valve to protect the property;
4. a regulator controlling the pressure of the gas flowing through the meter;
5. a filter to remove contaminants from the gas;
6. pipework connected to the inlet of the meter;
7. pipework connected to the outlet of the meter.

A meter module has the following attributes:
- module reference - the 'name' by which the module is referred to;
- service pressure - the pressure at which the gas arrives at the inlet of the module. This is often described as ranges (and subranges) of pressure:
  - LP - Low pressure;
  - MP - Medium pressure;
  - IP - Intermediate pressure;
  - HP - High pressure.
- inlet connection - the connection made with the the service pipe. This is described using the following attributes:
  - orientation - the lie of the connection e.g. 'horizontal left';
  - connection - a standard description of the connector used e.g. '(mm) PN16';
  - height - the position above the base at which the connection will be found;
  - size - the diameter of the connection;
- outlet connection - the connection made with the property. This is described using the following attributes:
  - orientation - the lie of the connection e.g. 'horizontal left';
  - connection - a standard description of the connector used e.g. '(mm) PN16';
  - height - the position above the base at which the connection will be found;
  - size - the diameter of the connection;
- dimensions - describing the physical size and positioning of the module using standard attributes of 'A' to 'H';
- weight - the weight of the module in kilograms;
- relief valve type - describes general characteristics of a relief valve;
- slamshut type - describes general characteristics of a slamshut valve;
- filter type - describes general characteristics of a filter;
- regulator type - describes general characteristics of a regulator;

A module can be requested with the following additional items:
- base - each module is associated with a single base;
- housing - each module is associated with a single housing;
- standard add-ons:
  - AMR - automatic meter reading device;
  - EMS - energy management system;
  - convertor - to display a live conversion on the module;
  - bypass - additional pipework that allows maintenance, replacement, etc. to take place on the meter without disrupting the flow of gas to the property.

A module can be associated with:
- a drawing - a graphical representation of the module;
- costs - the costs of buying and selling the module. This is described using the following attributes:
  - selling price - the price at which the module is sold;
  - delivery cost - the cost of delivery to the buyer;
  - region - the geographical region in which the costs are valid (different regions may have different pricing structures).
###### Meter
A meter is a component of the module used to measure the flow of gas to a property.
A meter has the following attributes:
- meter reference - the 'name' by which the meter is referred to;
- measuring capacity. This is described using the following attribute:
  - Qmax - the maximum volume of gas that can be passed through the meter per hour;
- dimensions - describing the physical size and positioning of the meter using standard attributes of 'A' to 'C' and 'Centres';
- weight - the weight of the meter in kilograms;
- connection type - a standard description of the type of the connector used e.g. 'PN16';
- meter type - a standard description of the method that the meter uses to measure flow e.g. 'Rotary'.

A meter can be associated with:
- a drawing - a graphical representation of the meter;
- costs - the costs of buying and selling the meter. This is described using the following attributes:
  - cost price - the price at which the meter is obtained;
  - delivery cost - the cost of delivery[1];
    [1] Is this the cost of delivery to NG Metering or cost of delivery to the Supplier?
- a manufacturer - the organisation that constructed the meter.
###### Housing
A housing encases a module. It is an optionally requested item on an enquiry.
A housing has the following attributes:
- housing reference - the 'name' by which the housing is referred to;
- dimensions - describing the physical characteristics of the housing:
  - length;
  - width;
  - height;
  - weight;
- doors - the number of doors in the housing;

A housing can be associated with:
- a module - each module may be associated with a single housing;
- a drawing - a graphical representation of the housing;
- a manufacturer - the organisation that constructed the housing.
- costs - the costs of buying and selling the housing. This is described using the following attributes:
- cost price - the price at which the housing is obtained;
  - selling price - the price at which the housing is sold to the customer;
  - labour cost – the cost of installing the housing (fixed at 10% of the selling price);
  - delivery cost - the cost of delivery1;
###### Base
A module is situated on a base (often a concrete slab}. It is an optionally requested item on an enquiry.
A base has the following attributes:
- base reference - the 'name' by which the base is referred to;
- dimensions - describing the physical characteristics of the base:
  - length;
  - width;
  - depth;
- standard dimensions 'A' to 'I'[2]
  [2] Why are there two sets of dimensions?

A base can be associated with:
- a module - each module may be associated with a single base;
- a drawing - a graphical representation of the base;
- costs - the costs of buying and selling the housing. This is described using the following attributes:
  - cost price - the price at which the housing is obtained;
  - selling price - the price at which the housing is sold to the customer;
  - delivery cost - the cost of delivery2;
###### Drawing
A drawing is a graphical representation of a physical object. The system stores drawings so that they may be displayed as part of a reporting object.

The system associates drawings with the following:
- module;
- meter;
- housing;
- base.
###### Standard add-ons
A number of standard (non-meter module specific) items may be requested to be included with a meter module:
- AMR - automatic meter reading device;
- EMS - energy management system;
- Converter - to display a live conversion on the module;
- bypass - additional pipework that allows maintenance, replacement, etc. to take place on the meter without disrupting the flow of gas to the property.

The system does not record the attributes of these items other than the fixed costs for the AMR, EMS and convertor items.
###### Pricing Data
With the exception of Standard add-ons (see Appendix ) all cost/pricing information may be regional i.e. the price for an item may differ according to the region in which the installation will take place. Regions are based on post-codes[3]. Where there are no applicable regional costs associated with an item, a non-regional price will be used for that item.
[3] Composition of postcode to region still unknown.
Where the system selects a meter module or associated item and a required supplier price is missing, the system is unable to produce a quotation. The enquiry is treated as a request for a Manual Quote that requires completion by D&Q.
Where the system selects a meter module or associated item and a required network price is missing, the system will produce a quotation but there will be a manual process during 'job' entry onto SAP to determine the relevant network costs.
Bypass pricing is handled off-line.
###### Tripartite Agreement
The Tripartite Agreement prevents quotations being produced for specified combinations of Suppliers, job types and postcodes. The system will record the Tripartite Agreement attributes as:
- Supplier – a reference to a Supplier that has not signed up to the Tripartite Agreement;
- Job Type - the Job Type(s) that the Supplier cannot be quoted for, one of:
  - Installation of new meters;
  - Request for OFGEM Meter Accuracy Test (OFMAT);
  - Exchange of meters;
  - Removal of meters, including 'Adversarial' removal of meters;
- Installation PostCode – the postcode where the installation is to take place.